## Slide 1: Complex circuit solution

## Slide 2
Draw out the schematic for the circuit
A
Choose a current orientation for a junction
A
I1
I2
I3
Entering a junction is (+)
Leaving a junction is (-)
According to Kirchhoff’s Current Rule
Equation 1: -I1 + I2 – I3 = 0

## Slide 3
Current through loops
Voltage through loops
Right Loop
According to Kirchhoff’s Voltage Rule
Equation 3: e1 + 8I1 – e2 – 8I3 + 8I1 = 0
24 + 8I1 – 12 – 8I3 + 8I1 = 0
16I1 – 8I3 = -12
I1
I1
I3
8Ω
8Ω
8Ω
ε1
ε2
V = IR
24V
12V
8Ω
I3
I2
ε2
According to Kirchhoff’s Voltage Rule
Equation 2: -e2 – 8I2 – 8I3 = 0
-12 – 8I2 – 8I3 = 0
-8I2 – 8I3 = 12
V = IR
Positive voltage
Negative voltage

## Slide 4
2nd x-1 = MATRIX
Choose “EDIT”, press enter
Change rows to 3 and columns to 4, press enter
Creating a matrix of 3 x 4

## Slide 5
Putting the three equations with three unknowns into a matrix
Equation 1: -I1 + I2 – I3 = 0
Equation 2: -8I2 – 8I3 = 12
Equation 3: 16I1 – 8I3 = -12
Enter the coefficient of I1, I2, and I3 and the constant in to the matrix

## Slide 6
Exit matrix mode by “2nd MODE” = “QUIT”
Reenter matrix mode by “2nd x-1” = MATRIX
Choose “MATH”
Go down to “B” rref
Press enter
Reenter matrix mode by “2nd x-1”
= MATRIX
Choose [A], press enter

## Slide 7
Press enter
All the currents are negative.
This means our original directions
for the current were incorrect.
Revise the direction of junction A.
A
I1
I2
I3
OLD
REVISED
A
I1
I2
I3
I1
I2
I3

## Slide 8
Calculating voltage drop across the resistors
V = IR
I1 = 0.9 A
I2 = 1.2 A
I3 = 0.3 A
V = (0.9 A)(8 Ω) = 7.2 V
V = (0.9 A)(8 Ω) = 7.2 V
V = (1.2 A)(8 Ω) = 9.6 V
V = (0.3 A)(8 Ω) = 2.4 V