## Slide 1: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Essential idea: One of the earliest uses for electricity was to produce light and heat. This technology continues to have a major impact on the lives of people around the world.
Nature of science: Although Ohm and Barlow published their findings on the nature of electric current around the same time, little credence was given to Ohm. Barlow’s incorrect law was not initially criticized or investigated. This is a reflection of the nature of academia of the time with physics in Germany being largely non-mathematical and Barlow held in high respect in England. It indicates the need for the publication and peer review of research findings in recognized scientific journals.
Notes: © 2014 By Timothy K. Lund

## Slide 2: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Understandings:
• Circuit diagrams
• Kirchhoff’s circuit laws
• Heating effect of current and its consequences
• Resistance expressed as R = V / I
• Ohm’s law
• Resistivity R = L / A
• Power dissipation
Notes: 2
© 2014 By Timothy K. Lund

## Slide 3: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Applications and skills:
• Drawing and interpreting circuit diagrams
• Identifying ohmic and non-ohmic conductors through a consideration of the V / I characteristic graph
• Solving problems involving potential difference, current, charge, Kirchhoff’s circuit laws, power, resistance and resistivity
• Investigating combinations of resistors in parallel and series circuits
• Describing ideal and non-ideal ammeters and voltmeters
• Describing practical uses of potential divider circuits, including the advantages of a potential divider over a series resistor in controlling a simple circuit
Notes: 3
© 2014 By Timothy K. Lund

## Slide 4: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Applications and skills:
• Investigating one or more of the factors that affect resistivity experimentally
Guidance:
• The filament lamp should be described as a non-ohmic device; a metal wire at a constant temperature is an ohmic device
• The use of non-ideal voltmeters is confined to voltmeters with a constant but finite resistance
• The use of non-ideal ammeters is confined to ammeters with a constant but non-zero resistance
• Application of Kirchhoff’s circuit laws will be limited to circuits with a maximum number of two source-carrying loops
Notes: 4
© 2014 By Timothy K. Lund

## Slide 5: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Data booklet reference:
• Kirchhoff’s circuit laws:
V = 0 (loop)
I = 0 (junction);
• R = V / I
• P = VI = I 2R = V 2/ R
• Rtotal = R1 + R2 + …
• 1 / Rtotal = 1 / R1 + 1 / R2 + …
•  = RA / L
Notes: 5
© 2014 By Timothy K. Lund

## Slide 6: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
International-mindedness:
• A set of universal symbols is needed so that physicists in different cultures can readily communicate ideas in science and engineering
Theory of knowledge:
• Sense perception in early electrical investigations was key to classifying the effect of various power sources, however this is fraught with possible irreversible consequences for the scientists involved. Can we still ethically and safely use sense perception in science research?
Notes: 6
© 2014 By Timothy K. Lund

## Slide 7: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Utilization:
• Although there are nearly limitless ways that we use electrical circuits, heating and lighting are two of the most widespread
• Sensitive devices can employ detectors capable of measuring small variations in potential difference and/or current, requiring carefully planned circuits and high precision components
Notes: 7
© 2014 By Timothy K. Lund

## Slide 8: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Aims:
• Aim 2: electrical theory and its approach to macro and micro effects characterizes much of the physical approach taken in the analysis of the universe
• Aim 3: electrical techniques, both practical and theoretical, provide a relatively simple opportunity for students to develop a feeling for the arguments of physics
• Aim 6: experiments could include (but are not limited to): use of a hot-wire ammeter as an historically important device; comparison of resistivity of a variety of conductors such as a wire at constant temperature, a filament lamp, or a graphite pencil;
Notes: 8
© 2014 By Timothy K. Lund

## Slide 9: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Aims:
• Aim 6: determination of thickness of a pencil mark on paper; investigation of ohmic and non-ohmic conductor characteristics; using a resistive wire wound and taped around the reservoir of a thermometer to relate wire resistance to current in the wire and temperature of wire
• Aim 7: there are many software and online options for constructing simple and complex circuits quickly to investigate the effect of using different components within a circuit
Notes: 9
© 2014 By Timothy K. Lund

## Slide 10: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Resistance
If you have ever looked inside an electronic device you have no doubt seen what a resistor looks like.
A resistor’s working part is usually made of carbon, which is a semiconductor.
The less carbon there is, the harder it is for current to flow through the resistor.
As the animation shows, carbon is spiraled away to cut down the cross-sectional area, thereby increasing the resistance to whatever value is desired.
Notes: 10
© 2006 By Timothy K. Lund

## Slide 11: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Resistance
Some very precise resistors are made of wire and are called wire-wound resistors.
And some resistors can be made to vary their resistance by tapping them at various places. These are called variable resistors and potentiometers.
Thermistors are temperature- dependent resistors, changing their resistance in response to their temperature.
Light-dependent resistors (LDRs) change their resistance in response to light intensity.
Notes: 11
© 2006 By Timothy K. Lund

## Slide 12: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
FYI
A reading of 0.L on an ohmeter means “overload”. The resistance is too high to record with the meter.
Resistance
Electrical resistance R is a measure of how hard it is for current to flow through a material. Resistance is measured in ohms () using an ohm-meter.
330.4
0.L
0.0
This resistor has a resistance of 330.4 .
Notes: 12
© 2006 By Timothy K. Lund

## Slide 13: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Resistance
The different types of resistors have different schematic symbols.
fixed-value resistor
variable resistor
potentiometer
2 leads
2 leads
3 leads
Notes: 13
© 2006 By Timothy K. Lund

## Slide 14: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Resistance
The different types of resistors have different schematic symbols.
thermister
light-dependent resistor (LDR)
2 leads
2 leads
As temperature increases resistance decreases
As brightness increases resistance decreases
Notes: 14
© 2006 By Timothy K. Lund

## Slide 15: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE:
A fixed resistor has a current of 18.2 mA when it has a 6.0 V potential difference across it. What is its resistance?
SOLUTION:
 R = V / I = 6.0 / 18.210-3 = 330 .
Resistance
The resistance R of a material is the ratio of the potential difference V across the material to the current I flowing through the material.
The units from the formula are (V A-1) which are called ohms ().
R = V / I
electric resistance
Orange = 3
Orange = 3
Brown = 1
Last color is number of zeros.
Notes: 15
© 2006 By Timothy K. Lund

## Slide 16: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Resistance
To understand electrical resistance, consider two identical milk shakes.
In the first experiment the straws have the same diameter, but different lengths.
In the second experiment the straws have the same length, but different diameters.
Note that R  L / A.
R  L
R  1 / A
Resistance is a measure of how hard it is to pass something through a material.
Notes: 16
© 2006 By Timothy K. Lund

## Slide 17: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Resistance
Of course conductors and resistors are not hollow like straws. And instead of milk shake current we have electrical current.
Even through solids R  L / A.
But R also depends on the material through which the electricity is flowing.
For example the exact same size of copper will have much less resistance than the carbon.
With the proportionality constant  we have equality:
R = L / A or  = RA / L
resistance equation
Notes: 17
© 2006 By Timothy K. Lund

## Slide 18: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Resistance
The Greek  is the resistivity of the particular material the resistor is made from. It is measured in m.
Resistivities and Temperature Coefficients for Various Materials at 20C
 (m)
 (C -1)
Material
 (m)
 (C -1)
Material
Conductors
Semiconductors
2.8210-8
4.2910-3
Aluminum
Carbon
360010-8
-5.010-4
1.7010-8
6.8010-3
Copper
Germanium
4.610-1
-5.010-2
1010-8
6.5110-3
Iron
Silicon
2.5102
-7.010-2
98.410-8
0.8910-3
Mercury
10010-8
0.4010-3
Nichrome
Nonconductors
7.810-8
6.010-3
Nickel
Glass
1012
1010-8
3.9310-3
Platinum
Rubber
1015
1.5910-8
6.110-3
Silver
Wood
1010
5.610-8
4.510-3
Tungsten
Notes: 18
© 2006 By Timothy K. Lund

## Slide 19: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: What is the resistance of a 0.00200 meter long carbon core resistor having a core diameter of 0.000100 m? Assume the temperature is 20 C.
r = d / 2 = 0.0001 / 2 = 0.00005 m.
A = r2 = (0.00005)2 = 7.85410-9 m2.
From the table  = 360010-8  m.
R = L / A
= (360010-8)(0.002) / 7.85410-9 = 9.17 .
Resistance
Note that resistance depends on temperature. The IBO does not require us to explore this facet of resistivity.
L
A
Notes: 19
© 2006 By Timothy K. Lund

## Slide 20: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
FYI
Ohm’s law applies to components with constant R.
Ohm’s law
The German Ohm studied resistance of materials in the 1800s and in 1826 stated:
“Provided the temperature is kept constant, the resistance of very many materials is constant over a wide range of applied potential differences, and therefore the potential difference is proportional to the current.”
In formula form Ohm’s law looks like this:
V  I
Ohm’s law
or V / I = CONST
or V = IR
Notes: 20
© 2006 By Timothy K. Lund

## Slide 21: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
EXAMPLE: Label appropriate V-I graphs with the following labels: ohmic, non-ohmic, R increasing, R decreasing, R constant.
SOLUTION:
First label the resistance dependence.
R = V / I so R is just the slope of the V vs. I graph.
Ohm’s law states the R is constant. Thus only one graph is ohmic.
Ohm’s law – ohmic and non-ohmic behavior
A material is considered ohmic if it behaves according to Ohm’s law. In other words the resistance stays constant as the voltage changes.
V
I
V
I
V
I
R
R
R
ohmic
non-ohmic
non-ohmic
Notes: 21
© 2006 By Timothy K. Lund

## Slide 22: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
EXAMPLE: The graph shows the applied voltage V vs. resulting current I through a tungsten filament lamp.
Find R when I = 0.5 mA and 1.5 mA. Is this filament ohmic or non-ohmic?
SOLUTION:
At 0.5 mA: V = 0.08 V
R = V / I = 0.08 / 0.510-3 = 160 .
At 1.5 mA: V = 0.6 V
R = V / I = 0.6 / 1.510-3 = 400 .
Ohm’s law – ohmic and non-ohmic behavior
Since R is not constant the filament is non-ohmic.
Notes: 22
© 2006 By Timothy K. Lund

## Slide 23: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
EXAMPLE: The graph shows the applied voltage V vs. resulting current I through a tungsten filament lamp.
Explain why a lamp filament might be non-ohmic.
SOLUTION:
The temperature coefficient for tungsten is positive, typical for conductors.
Therefore, the hotter the filament the higher R.
But the more current, the hotter a lamp filament burns.
Thus, the bigger the I the bigger the R.
Ohm’s law – ohmic and non-ohmic behavior
 (m)
 (C -1)
Material
5.610-8
4.510-3
Tungsten
Notes: 23
© 2006 By Timothy K. Lund

## Slide 24: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
EXAMPLE: The I-V characteristic is shown for a non-ohmic compo- nent. Sketch in the I-V character- istic for a 40  ohmic component in the range of 0.0 V to 6.0 V.
SOLUTION:
”Ohmic” means V = IR and R is constant (and the graph is linear).
Thus V = I40 or I = V / 40.
If V = 0, I = 0 / 40 = 0.0.
If V = 6, I = 6 / 40 = 0.15 A.
But 0.15 A = 150 mA.
Ohm’s law – ohmic and non-ohmic behavior
Notes: 24
© 2006 By Timothy K. Lund

## Slide 25: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
FYI
This power represents the energy per unit time delivered to, or consumed by, an electrical component having a current I and a potential difference V.
Power dissipation
Recall that power is the rate at which work is being done. Thus P = W / t.
From Topic 5.1 we learned that W = qV.
Thus
P = W / t
P = qV / t
P = (q / t)V
P = IV.
Notes: 25
© 2006 By Timothy K. Lund

## Slide 26: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Power dissipation
PRACTICE: Use the definition of resistance R = V / I. together with the one we just derived (P = VI) to derive the following two formulas:
(a) P = I 2R
(b) P = V 2/ R.
SOLUTION:
(a) From R = V / I we get V = IR.
P = IV = I ( IR ) = I 2R.
(b) From R = V / I we get I = V / R.
P = IV = (V / R) (V) = V 2/ R.
P = VI = I 2R = V 2/ R
electrical power
Notes: 26
© 2006 By Timothy K. Lund

## Slide 27: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE:
The graph shows the V-I characteristics of a tungsten filament lamp.
What is its power consumption at I = 0.5 mA and at I = 1.5 mA?
SOLUTION:
At 0.5 mA, V = 0.08 V.
P = IV = (0.510-3)(0.08) = 4.010-5 W.
At 1.5 mA, V = 0.6 V.
P = IV = (1.510-3)(0.6) = 9.010-4 W.
Power dissipation
Notes: 27
© 2006 By Timothy K. Lund

## Slide 28: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Electric circuits
An electric circuit is a set of conductors (like wires) and components (like resistors, lights, etc.) connected to an electrical voltage source (like a cell or a battery) in such a way that current can flow in complete loops.
Here are two circuits consisting of cells, resistors, and wires.
Note current flowing from (+) to (-) in each circuit.
solder joints
single-loop circuit
triple-loop circuit
Notes: © 2006 By Timothy K. Lund

## Slide 29: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Circuit diagrams
A complete circuit will always contain a cell or a battery.
The schematic diagram of a cell is this:
A battery is just a group of cells connected in series:
If each cell is 1.5 V, then the battery above is 3(1.5) = 4.5 V. What is the voltage of your calculator battery?
A fixed-value resistor looks like this:
The schematic of a fixed-value resistor looks like this:
this is really a cell…
this is a battery…
this is a resistor…
this is the same battery…
Notes: © 2006 By Timothy K. Lund

## Slide 30: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
EXAMPLE: Draw schematic diagrams of each of the following circuits:
SOLUTION:
Drawing and interpreting circuit diagrams
Notes: © 2006 By Timothy K. Lund

## Slide 31
Investigating combinations of resistors in series
Resistors can be connected to one another in series, which means one after the other.
Note that there is only one current I and that I is the same for all series components.
Conservation of energy tells us q = qV1 + qV2 + qV3.
Thus  = IR1 + IR2 + IR3 from Ohm’s law V = IR
 = I(R1 + R2 + R3) factoring out I
 = I(R), where R = R1 + R2 + R3.
R1
R2
R3
R = R1 + R2 + …
equivalent resistance in series

Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Notes: © 2006 By Timothy K. Lund

## Slide 32
EXAMPLE: Three resistors of 330  each are connected to a 6.0 V battery in series as shown.
(a) What is the circuit’s equivalent resistance?
(b) What is the current in the circuit?
SOLUTION:
(a) In series, R = R1 + R2 + R3 so that
R = 330 + 330 + 330 = 990 .
(b) Since the voltage on the entire circuit is 6.0 V, and since the total resistance is 990 , from Ohm’s law we have I = V / R = 6 / 990 = 0.0061 A.
Investigating combinations of resistors in series
Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
R1
R2
R3

Notes: © 2006 By Timothy K. Lund

## Slide 33
FYI
In series the V’s are different if the R’s are different.
EXAMPLE: Three resistors of 330  each are connected to a 6.0 V battery in series as shown.
(c) What is the voltage on each resistor?
SOLUTION:
(c) The current I we just found is the same everywhere. Thus each resistor has a current of I = 0.0061 A.
From Ohm’s law, each resistor has a voltage given by V = IR = (0.0061)(330) = 2.0 V.
Investigating combinations of resistors in series
Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
R1
R2
R3

Notes: © 2006 By Timothy K. Lund

## Slide 34: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Investigating combinations of resistors in parallel
Resistors can also be in parallel.
In this circuit each resistor is connected directly to the cell.
Thus each resistor has the same voltage V and V is the same for all parallel components.
We can then write  = V1 = V2 = V3  V.
But there are three currents I1, I2, and I3.
Since the total current I passes through the cell we see that I = I1 + I2 + I3.
If R is the equivalent or total resistance of the three resistors, then I = I1 + I2 + I3 becomes
 / R = V1 / R1 + V2 / R2 + V3 / R3 Ohm’s law I = V / R
R1
R2
R3

Notes: © 2006 By Timothy K. Lund

## Slide 35: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Investigating combinations of resistors in parallel
Resistors can also be in parallel.
In this circuit each resistor is connected directly to the cell.
Thus each resistor has the same voltage V and V is the same for all parallel components.
From  = V1 = V2 = V3  V
and  / R = V1 / R1 + V2 / R2 + V3 / R3,
we get V / R = V / R1 + V / R2 + V / R3.
Thus the equivalent resistance R is given by
R1
R2
R3

1 / R = 1 / R1 + 1 / R2 + …
equivalent resistance in parallel
Notes: © 2006 By Timothy K. Lund

## Slide 36: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
EXAMPLE: Three resistors of 330  each are connected to a 6.0 V cell in parallel as shown.
(a) What is the circuit’s resistance?
(b) What is the voltage on each resistor?
SOLUTION:
(a) In parallel, 1 / R = 1 / R1 + 1 / R2 + 1 / R3 so that
1 / R = 1 / 330 + 1 / 330 + 1 / 330 = 0.00909.
Thus R = 1 / 0.00909 = 110 .
(b) The voltage on each resistor is 6.0 V, since the resistors are in parallel. (Each resistor is clearly directly connected to the battery).
Investigating combinations of resistors in parallel
R1
R2
R3

Notes: © 2006 By Timothy K. Lund

## Slide 37: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
FYI
In parallel the I’s are different if the R’s are different.
EXAMPLE: Three resistors of 330  each are connected to a 6.0 V cell in parallel as shown.
(c) What is the current in each resistor?
SOLUTION:
(c) Using Ohm’s law (I = V / R):
I1 = V1 / R1 = 6 / 330 = 0.018 A.
I2 = V2 / R2 = 6 / 330 = 0.018 A.
I3 = V3 / R3 = 6 / 330 = 0.018 A.
Investigating combinations of resistors in parallel
R1
R2
R3

Notes: © 2006 By Timothy K. Lund

## Slide 38: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
FYI
Be sure to position the voltmeter across the desired resistor in parallel.
PRACTICE: Draw a schematic diagram for this circuit:
SOLUTION:
Circuit diagrams - voltmeters are connected in parallel
1.06
Notes: © 2006 By Timothy K. Lund

## Slide 39: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
EXAMPLE:
A battery’s voltage is measured as shown.
(a) What is the uncertainty in it’s measurement?
SOLUTION:
For digital devices always use the place value of the least significant digit as your raw uncertainty.
For this voltmeter the voltage is measured to the tenths place so we give the raw uncertainty a value of ∆V = 0.1 V.
Circuit diagrams - voltmeters are connected in parallel
tenths place
09.4
00.0
Notes: 39
© 2006 By Timothy K. Lund

## Slide 40: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
FYI
When using a voltmeter the red lead is placed at the point of highest potential.
EXAMPLE:
A battery’s voltage is measured as shown.
(b) What is the fractional error in this measurement?
SOLUTION: Fractional error is just V / V. For this particular measurement we then have
V / V = 0.1 / 9.4 = 0.011 (or 1.1%).
Circuit diagrams - voltmeters are connected in parallel
09.4
Notes: 40
© 2006 By Timothy K. Lund

## Slide 41: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Circuit diagrams - voltmeters are connected in parallel
Consider the simple circuit of battery, lamp, and wire.
To measure the voltage of the circuit we merely connect the voltmeter while the circuit is in operation.
01.6
00.0
cell
lamp
voltmeter
in parallel
Notes: 41
© 2006 By Timothy K. Lund

## Slide 42: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Circuit diagrams - ammeters are connected in series
To measure the current of the circuit we must break the circuit and insert the ammeter so that it intercepts all of the electrons that normally travel through the circuit.
00.2
00.0
cell
lamp
ammeter
in series
Notes: 42
© 2006 By Timothy K. Lund

## Slide 43: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
FYI
Be sure to position the ammeter between the desired resistors in series.
PRACTICE: Draw a schematic diagram for this circuit:
SOLUTION:
.003
Circuit diagrams - ammeters are connected in series
the circuit must be temporarily broken to insert the ammeter
Notes: © 2006 By Timothy K. Lund

## Slide 44: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
FYI
This circuit is a combination series-parallel. In a later slide you will learn how to find the equivalent resistance of the combo circuit.
PRACTICE: Draw a schematic diagram for this circuit:
SOLUTION:
Circuit diagrams
Notes: © 2006 By Timothy K. Lund

## Slide 45: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Ideal voltmeters -   resistance
Voltmeters are connected in parallel.
The voltmeter reads the voltage of only the component it is in parallel with.
The green current represents the amount of current the battery needs to supply to the voltmeter in order to make it register.
The red current is the amount of current the battery supplies to the original circuit.
In order to NOT ALTER the original properties of the circuit, ideal voltmeters have extremely high resistance ( ) to minimize the green current.
Notes: © 2006 By Timothy K. Lund

## Slide 46: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Ideal ammeters - 0  resistance
Ammeters are connected in series.
The ammeter is supposed to read the current of the original circuit.
In order to NOT ALTER the original properties of the circuit, ideal ammeters have extremely low resistance (0 ) to minimize the effect on the red current.
Notes: © 2006 By Timothy K. Lund

## Slide 47: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Potential divider circuits
Consider a battery of  = 6 V. Suppose we have a light bulb that can only use three volts. How do we obtain 3 V from a 6 V battery?
A potential divider is a circuit made of two (or more) series resistors that allows us to tap off any voltage we want that is less than the battery voltage.
The input voltage is the emf of the battery.
The output voltage is the voltage drop across R2.
Since the resistors are in series R = R1 + R2.
potential divider
R1
R2
Notes: © 2006 By Timothy K. Lund

## Slide 48: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Potential divider circuits
Consider a battery of  = 6 V. Suppose we have a light bulb that can only use three volts. How do we obtain 3 V from a 6 V battery?
From Ohm’s law the current I of the divider is given by I = VIN / R = VIN / (R1 + R2).
But VOUT = V2 = IR2 so that
VOUT = IR2
= R2VIN / (R1 + R2).
potential divider
R1
R2
VOUT = VIN [ R2 / (R1 + R2) ]
potential divider
Notes: © 2006 By Timothy K. Lund

## Slide 49: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
FYI
The bigger R2 is in comparison to R1, the closer VOUT is in proportion to the total voltage.
PRACTICE:
Find the output voltage if the battery has an emf of 9.0 V, R1 is a 2200  resistor, and R2 is a 330  resistor.
SOLUTION:
Use VOUT = VIN [ R2 / (R1 + R2) ]
VOUT = 9 [ 330 / (2200 + 330) ]
VOUT = 9 [ 330 / 2530 ] = 1.2 V.
Potential divider circuits
Notes: © 2006 By Timothy K. Lund

## Slide 50: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE:
Find the value of R2 if the battery has an emf of 9.0 V, R1 is a 2200  resistor, and we want an output voltage of 6 V.
SOLUTION:
Use the formula VOUT = VIN [ R2 / (R1 + R2) ]. Thus
6 = 9 [ R2 / (2200 + R2) ]
6(2200 + R2) = 9R2
13200 + 6R2 = 9R2
13200 = 3R2
R2 = 4400 
Potential divider circuits
Notes: © 2006 By Timothy K. Lund

## Slide 51: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: A light-dependent resistor (LDR) has R = 25  in bright light and R = 22000  in low light. An electronic switch will turn on a light when its p.d. is above 7.0 V. What should the value of R1 be?
SOLUTION: Use VOUT = VIN [ R2 / (R1 + R2) ]. Thus
7 = 9 [ 22000 / (R1 + 22000) ]
7(R1 + 22000) = 9(22000)
7R1 + 154000 = 198000
7R1 = 44000
R1 = 6300  (6286)
Potential divider circuits
Notes: © 2006 By Timothy K. Lund

## Slide 52: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: A thermistor has a resistance of 250  when it is in the heat of a fire and a resistance of 65000  when at room temperature. An electronic switch will turn on a sprinkler system when its p.d. is above 7.0 V.
(a) Should the thermistor be R1 or R2?
SOLUTION:
Because we want a high voltage at a high temperature, and because the thermistor’s resistance decreases with temperature, it should be placed at the R1 position.
Potential divider circuits
Notes: © 2006 By Timothy K. Lund

## Slide 53: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: A thermistor has a resistance of 250  when it is in the heat of a fire and a resistance of 65000  when at room temperature. An electronic switch will turn on a sprinkler system when its p.d. is above 7.0 V.
(b) What should R2 be?
SOLUTION: In fire the thermistor is R1 = 250 .
7 = 9 [ R2 / (250 + R2) ]
7(250 + R2) = 9R2
1750 + 7R2 = 9R2  R2 = 880  (875)
Potential divider circuits
Notes: © 2006 By Timothy K. Lund

## Slide 54: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: A filament lamp is rated at “4.0 V, 0.80 W” on its package. The potentiometer has a resistance from X to Z of 24  and has linear variation.
(a) Sketch the variation of the p.d. V vs. the current I for a typical filament lamp. Is it ohmic?
SOLUTION: Since the temperature increases with the current, so does the resistance.
But from V = IR we see that R = V / I, which is the slope.
Thus the slope should increase with I.
V
I
ohmic means linear
non-ohmic
Potential divider circuits
Notes: © 2006 By Timothy K. Lund

## Slide 55: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: A filament lamp is rated at “4.0 V, 0.80 W” on its package. The potentiometer has a resistance from X to Z of 24  and has linear variation.
(b) The potentiometer is adjusted so that the meter shows 4.0 V. Will it’s contact be above Y, below Y, or exactly on Y?
SOLUTION: The circuit is acting like a potential divider with R1 being the resistance between X and Y and R2 being the resistance between Y and Z.
Since we need VOUT = 4 V, and since VIN = 7 V, the contact must be adjusted above the Y.
Potential divider circuits
R1
R2
Notes: © 2006 By Timothy K. Lund

## Slide 56: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: A filament lamp is rated at “4.0 V, 0.80 W” on its package. The potentiometer has a resistance from X to Z of 24  and has linear variation.
(c) The potentiometer is adjusted so that the meter shows 4.0 V. What are the current and the resistance of the lamp at this instant?
SOLUTION: P = 0.80 W and V = 4.0 V.
From P = IV we get 0.8 = I(4) so that I = 0.20 A.
From V = IR we get 4 = 0.2R so that R = 20. .
You could also use P = I 2R for this last one.
Potential divider circuits
R1
R2
Notes: © 2006 By Timothy K. Lund

## Slide 57: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: A filament lamp is rated at “4.0 V, 0.80 W” on its package. The potentiometer has a resistance from X to Z of 24  and has linear variation.
(d) The potentiometer is adjusted so that the meter shows 4.0 V. What is the resistance of the Y-Z portion of the potentiometer?
SOLUTION: Let R1 = X to Y and R2 = Y to Z resistance.
Then R1 + R2 = 24 so that R1 = 24 – R2.
From VOUT = VIN [ R2 / (R1 + R2) ] we get
4 = 7 [ R2 / (24 – R2 + R2) ]
Potential divider circuits
R1
R2
 R2 = 14  (13.71).
Notes: © 2006 By Timothy K. Lund

## Slide 58: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: A filament lamp is rated at “4.0 V, 0.80 W” on its package. The potentiometer has a resistance from X to Z of 24  and has linear variation.
(e) The potentiometer is adjusted so that the meter shows 4.0 V. What is the current in the Y-Z portion of the potentiometer?
SOLUTION:
V2 = 4.0 V because it is in parallel with the lamp.
I2 = V2 / R2
= 4 / 13.71 = 0.29 A
Potential divider circuits
R1
R2
Notes: © 2006 By Timothy K. Lund

## Slide 59: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: A filament lamp is rated at “4.0 V, 0.80 W” on its package. The potentiometer has a resistance from X to Z of 24  and has linear variation.
(f) The potentiometer is adjusted so that the meter shows 4.0 V. What is the current in the ammeter?
SOLUTION: The battery supplies two currents.
The red current is 0.29 A because it is the I2 we just calculated in (e).
The green current is 0.20 A found in (c).
The ammeter has both so I = 0.29 + 0.20 = 0.49 A.
Potential divider circuits
R1
R2
Notes: © 2006 By Timothy K. Lund

## Slide 60: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: A battery is connected to a 25-W lamp as shown.
What is the lamp’s resistance?
SOLUTION:
Suppose we connect a voltmeter to the circuit.
We know P = 25 W.
We know V = 1.4 V.
From P = V 2 / R we get
R = V 2/ P = 1.4 2 / 25 = 0.078 .
01.4
00.0
Solving problems involving circuits
Notes: 60
© 2006 By Timothy K. Lund

## Slide 61: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: Which circuit shows the correct setup to find the V-I characteristics of a filament lamp?
SOLUTION:
The voltmeter must be in parallel with the lamp.
It IS, in ALL cases.
The ammeter must be in series with the lamp and must read only the lamp’s current.
The correct response is B.
two currents
no currents
short circuit!
lamp current
Solving problems involving circuits
Notes: © 2006 By Timothy K. Lund

## Slide 62: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: A non-ideal voltmeter is used to measure the p.d. of the 20 k resistor as shown. What will its reading be?
SOLUTION: There are two currents in the circuit because the voltmeter does not have a high enough resistance to prevent the green one from flowing.
The 20 k resistor is in parallel with the 20 k so that
1 / R = 1 / 20000 + 1 / 20000 = 2 / 20000.
R = 20000 / 2 = 10 k.
But then we have two 10 k resistors in series and each takes half the battery voltage, or 3 V.
equivalent ckt
Solving problems involving circuits
Notes: © 2006 By Timothy K. Lund

## Slide 63: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: All three circuits use the same resistors and the same cells.
Which one of the following shows the correct ranking for the currents passing through the cells?
SOLUTION: The bigger the R the smaller the I.
2R
0.5R
R
0.5R
1.5R
parallel
series
combo
Highest I
Lowest I
Middle I
Solving problems involving circuits
Notes: © 2006 By Timothy K. Lund

## Slide 64: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: The voltmeter has infinite resistance.
What are the readings on the voltmeter when the switch is open and closed?
SOLUTION:
With the switch open the green R is not part of the circuit. Red and orange split the battery emf.
With the switch closed the red and green are in parallel and are (1/2)R.
Solving problems involving circuits
E
Notes: © 2006 By Timothy K. Lund

## Slide 65: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Kirchhoff’s rules – junction, branch, and loop
”Solving” a circuit consists of finding the voltages and currents of all of its components.
Consider the following circuit containing a few batteries and resistors:
A junction is a point in a circuit where three or more wires are connected together.
A branch is all the wire and all the components connecting one junction to another.
A loop is all the wire and all the components in a complete circle.
Gustav Robert Kirchhoff
Notes: 65
© 2006 By Timothy K. Lund

## Slide 66: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
FYI
If a current turns out to have a negative solution, you will interpret that as meaning that it flows in the opposite direction.
Kirchhoff’s rules – the rule for current I
”Solving” a circuit consists of finding the voltages and currents of all of its components.
STEP 1: Assign a current to each branch.
If you have a good idea which way it flows, choose that direction.
If you don’t, an arbitrary direction will do just fine.
I1
I2
I3
Notes: 66
© 2006 By Timothy K. Lund

## Slide 67: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Kirchhoff’s rules – the rule for current I
”Solving” a circuit consists of finding the voltages and currents of all of its components.
If a current enters a junction it is a “gain” and is assigned a POSITIVE value. If a current leaves a junction it is a “loss” and is assigned a NEGATIVE value.
For the TOP junction, I1 and I3 are both POSITIVE and I2 is NEGATIVE.
For the BOTTOM junction, I1 and I3 are both NEGATIVE and I2 is POSITIVE.
I1
I2
I3
Notes: 67
© 2006 By Timothy K. Lund

## Slide 68: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Kirchhoff’s rules – the rule for current I
”Solving” a circuit consists of finding the voltages and currents of all of its components.
From conservation of charge the sum of the currents at each junction is zero.
STEP 2: Use Kirchhoff’s rule for I for each junction.
Each JUNCTION yields its own equation:
TOP: I1 – I2 + I3 = 0.
BOTTOM: I2 – I1 – I3 = 0.
I1
I2
I3
I = 0 (junction)
Kirchhoff’s rule for I
Notes: 68
© 2006 By Timothy K. Lund

## Slide 69: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Kirchhoff’s rules – the rule for voltage V
”Solving” a circuit consists of finding the voltages and currents of all of its components.
Give each resistor a voltage V and each cell or battery an emf .
Cells and batteries increase the energy of the current, resistors decrease the energy.
Since the energy is qV (or q), if we sum up all the energy gains and losses in each LOOP we must get zero.
We can go either CW or CCW – it doesn’t matter.
I1
I2
I3
V3
V1
V2
V4
1
2
Notes: 69
© 2006 By Timothy K. Lund

## Slide 70: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Kirchhoff’s rules – the rule for voltage V
”Solving” a circuit consists of finding the voltages and currents of all of its components.
If our loop goes in the direction of the branch current assigned earlier, the resistor energy change is negative.
If our loop goes against the branch current, the sign is reversed for the resistor.
For our loop we see that we have –qV1 and –qV2 and –qV4.
I1
I2
I3
V3
V1
V2
V4
1
2
negative
positive
Notes: 70
© 2006 By Timothy K. Lund

## Slide 71: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
Kirchhoff’s rules – the rule for voltage V
”Solving” a circuit consists of finding the voltages and currents of all of its components.
If our loop goes through a cell from negative to positive, the cell energy change is positive.
If our loop goes from positive to negative through a cell the energy change is negative.
For our loop we see that we have +q1 and –q2.
I1
I2
I3
V3
V1
V2
V4
1
2
positive
negative
Notes: 71
© 2006 By Timothy K. Lund

## Slide 72: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
FYI
The qs all cancel.
Kirchhoff’s rules – the rule for voltage V
”Solving” a circuit consists of finding the voltages and currents of all of its components.
From conservation of energy the sum of the voltages in each loop is zero.
STEP 3: Use Kirchhoff’s rule for V for each loop.
For our loop we have
–V1 + 1 + –V2 + –V4 + –2 = 0.
I1
I2
I3
V3
V1
V2
V4
1
2
V = 0 (loop)
Kirchhoff’s rule for V
Notes: 72
© 2006 By Timothy K. Lund

## Slide 73: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
PRACTICE: Using the voltage rule write the equation for the other loop.
SOLUTION:
–2 + –V3 + –V4 = 0.
Kirchhoff’s rules – the rule for voltage V
”Solving” a circuit consists of finding the voltages and currents of all of its components.
From conservation of energy the sum of the voltages in each loop is zero.
I1
I2
I3
V3
V1
V2
V4
1
2
V = 0 (loop)
Kirchhoff’s rule for V
negative
negative
Notes: 73
© 2006 By Timothy K. Lund

## Slide 74: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
EXAMPLE: Suppose each of the resistors is R = 2.0 , and the emfs are 1 = 12 V and 2 = 6.0 V. Find the voltages and the currents of the circuit.
SOLUTION: Use Ohm’s law: V = IR for the resistors.
From the rule for I we have I1 – I2 + I3 = 0.
From the rule for V we have
–V1 + –V2 + –V4 + 1 + – 2 = 0,
– 2 – V3 – V4 = 0.
From Ohm’s law we have
–2I1 + –2I1 + –2I2 + 12 + –6 = 0
– 6 – 2I3 – 2I2 = 0.
Kirchhoff’s rules – solving the circuit
I1
I2
I3
V3
V1
V2
V4
1
2
Notes: 74
© 2006 By Timothy K. Lund

## Slide 75: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
EXAMPLE: Suppose each of the resistors is R = 2.0 , and the emfs are 1 = 12 V and 2 = 6.0 V. Find the voltages and the currents of the circuit.
SOLUTION:
We now have three equations in I.
I1 – I2 + I3 = 0  I3 = I2 – I1.
–2I1 + –2I1 + –2I2 + 12 + –6 = 0
 6 = 4I1 + 2I2  3 = 2I1 + I2.
– 6 – 2I3 – 2I2 = 0
 6 = -2I2 + -2I3  3 = -I2 + -I3.
Kirchhoff’s rules – solving the circuit
I1
I2
I3
V3
V1
V2
V4
1
2
Notes: 75
© 2006 By Timothy K. Lund

## Slide 76: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
EXAMPLE: Suppose each of the resistors is R = 2.0 , and the emfs are 1 = 12 V and 2 = 6.0 V. Find the voltages and the currents of the circuit.
SOLUTION:
Now eliminate variables one by one.
(1) I3 = I2 – I1. (2) 3 = 2I1 + I2. (3) 3 = -I2 + -I3.
(1) into (3) eliminates I3:
3 = -I2 + - (I2 – I1) or 3 = -2I2 + I1.
Then I1 = 3 + 2I2.
Placing into (2) yields
3 = 2(3 + 2I2) + I2 so that
3 = 6 + 4I2 + I2  I2 = -0.6 A.
Kirchhoff’s rules – solving the circuit
I1
I2
I3
V3
V1
V2
V4
1
2
Notes: 76
© 2006 By Timothy K. Lund

## Slide 77: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
EXAMPLE: Suppose each of the resistors is R = 2.0 , and the emfs are 1 = 12 V and 2 = 6.0 V. Find the voltages and the currents of the circuit.
SOLUTION:
Once you have one, you have them all by substitution:
(1) I3 = I2 – I1. (2) 3 = 2I1 + I2. (3) 3 = -I2 + -I3.
Putting I2 = -0.6 A into (2) yields
3 = 2I1 + -0.6  I1 = 1.8 A.
Putting I1 and I2 into (1) yields
I3 = -0.6 – 1.8 = -2.4 A.
Since I2 and I3 are negative, we chose the wrong directions.
Kirchhoff’s rules – solving the circuit
I1
I2
I3
V3
V1
V2
V4
1
2
Notes: 77
© 2006 By Timothy K. Lund

## Slide 78: Topic 5: Electricity and magnetism 5.2 – Heating effect of electric currents
EXAMPLE: Suppose each of the resistors is R = 2.0 , and the emfs are 1 = 12 V and 2 = 6.0 V. Find the voltages and the currents of the circuit.
SOLUTION:
Finally, we can redraw our currents:
From Ohm’s law we calculate our resistor voltages:
V1 = 1.8(2) = 3.6 V.
V2 = 1.8(2) = 3.6 V.
V3 = 2.4(2) = 4.8 V.
V4 = 0.6(2) = 1.2 V.
Use both of Kirchhoff’s rules to check junctions and loops.
Kirchhoff’s rules – solving the circuit
1.8 A
0.6 A
2.4 A
4.8 V
3.6 V
3.6 V
1.2 V
12 V
6 V
V3
V1
V2
V4
Notes: 78
© 2006 By Timothy K. Lund